| The installation instruction of W211 06-09 Door mirror cover w/LED (arrow type) + Manner light |  |
| --- | --- |
|  | The following parts are included in the kit: (1) (2) (3) (4) (5) (6) (7) (8) |  |
| . | There are two models of the factory door mirror for W211 06-09 E CLASS, one is with manner light another is without manner light. The following are two methods of installation instruction for the new arrow type Howell’s mirror. A. With manner light 1. Remove the original mirror glass 2. Remove the holder of mirror glass 3. Remove the original mirror cover and no need to remove the main component of mirror from the door |  |
|  | 4. To connect the wire 5 to the arrow type indicator light and the wire 4 to manner light of the new Howell’s mirror cover then use screws 8 to screw the mirror cover with arrow type light + manner light onto the main component of the original mirror. Please bottom the warning switch before to plug to connect the power of the indicator and manner light. B. Without manner light 1. Step 1 and 2 same as above with manner light. 2. Step 3 remove the original mirror cover 3. Remove the inside door panel and find the position and also need to remove the component of the door light of mirror from the door 4. To find the wire1 & wire6 from the original wire harness with white plug then cut these two wires and leave the white plug along. Next to take the component of the wire (6) to connect with the wire1 & wire6 then use the extra wire (3) to connect the original door manner light on the front door. Now the wire of manner light is installed completion. Please bottom the warning switch before to plug to connect the power of the indicator and manner light. 5. Reinstall the inside door panel of front door and new door mirror assy. Now the new door mirror with arrow type indicator are installed completion. |  |