| The installation instruction of W221 & W219 05-08 Door mirror cover w/LED (arrow type) + Manner light |  |
| --- | --- |
|  | The following parts are included in the kit: Cover (1) x 2 Frame(1) x 2 Wire (2) × 2 Wire (3) × 2 Screw (4) x 10 |  |
| . | 1. Remove the original door mirror cover 2. Remove the holder of mirror glass 3. Remove the original mirror cover and no need to remove the main Component of the mirror from the door |  |
|  | 4. To connect the wire 2 to the arrow type indicator light and the wire 3 to manner light of the new Howell’s mirror cover then use screws 4 to screw the mirror cover with arrow type light + manner light onto the main component of the original mirror. Please bottom the warning switch before to plug to connect the power of the indicator and manner light. |  |