| The installation instruction of W211 02-05 Door mirror cover w/LED (arrow type) + Manner light |  |
| --- | --- |
|  | The following parts are included in the kit: Wire (1) × 2 Wire (2) × 2 Wire (3) × 2 Splice connector x 4 |  |
| . | 1. Remove the original door mirror cover 2. Remove the main component of the original door mirror |  |
|  | 3. Remove the inside door panel of the front door 4. Install manner light: There are two types of original door mirror: A. without manner light B. with manner light. Below are the methods of wire connection. A. Without manner light To find the wire3 (white/black) & wire4 (black) from the original wire harness with white plug then cut these two wires and leave the white plug along. Next to take the component of the wire (2) to connect with the wire3 & wire4 then use the extra wire (3) to connect the original door manner light on the front door. Now the wire of manner light is installed completion. Please bottom the warning switch before to plug to connect the power of the indicator and manner light. B.With manner light Owing to the original door mirror with light ready has manner light. Just remove the original mirror cover and install the new mirror cover with arrow type light. Now it is installed completion. Please bottom the warning switch before to plug to connect the power of the indicator and manner light. 5. To connect the indicator light on the mirror cover, please check the point 1 & 2 of the plug on the mirror cover to face the point 1 & 2 of the plug on the main component of the door mirror then connect and fit the new mirror cover with arrow type light onto the main component. 6. Reinstall the inside door panel of front door and new door mirror assy. Now the new door mirror with arrow type indicator are installed completion. |  |