INSTALLATION INSTRUCTION:

REPLACEMENT OF MIRROR COVERS WITH LED TURN SIGNAL

FOR W163 M CLASS 1998-2001

1. Remove the factory mirror cover, Use a flat blade screwdriver to nudge the factory mirror cover fingers ( four points ) from the mounting tabs behind the mirrors then release the factory mirror covers. See picture 1, 2, 3, 4

picture1                 picture 2              picture 3           picture 4

2. Remove the factory mirror assembly, Use 8 mm wrench to remove the nuts behind

the sail cover, unplug the electrical connecter of the power mirrors. Pull the mirror assembly slowly straight away from the door.

3. Routing LED signal wire through the factory mirrors assembly. Fish the wires

from mirror cover with LED down through the center pin of the hinge along side

the factory wires which power of the mirrors. Lift up the flat gasket up over the mounting studs and find the wires of the mirror cover with LED in the bottom part of the hinge and grab with the pliers. Caution: Don’t pull tight! Leave slack inside the

mirror covers with LED. See picture 5

picture 5

4. Install mirror cover with LED onto the factory mirror assembly. Attach the mounting  point of mirror cover with LED nearest the hinge and snap into place. With remaining

mounting points lined up, squeeze the mirror covers with LED towards the mirror assembly until the mounting points to make connection. See picture 6

picture 6

5. Insert pins from LED wires of mirror covers to male connector of extension wires.

See picture 7

picture 7

6. Re-install the mirror covers with LED + factory mirror assembly onto the correct position of the door. See picture 8

picture 8

7. Connect wires at sidelight. The extension wires need to be routed through the door and fender to the sidelight to make the connection using the supplied wire tap connectors ( reminder: squeeze the metal core with pliers then close plastic cover ). Wrap securely with quality black electricians tape then plug-in the sidelight module and reinstall in fender. See picture 9, 10

picture 9                            picture 10

8. And that’s it! The mirror covers with LED are upgrade and completed.

picture11