INSTALLATION INSTRUCTION:

REPLACEMENT OF MIRROR COVERS WITH LED TURN SIGNAL

FOR W463 G CLASS 1991-2001

1. The following parts are included in the kit:

|  | Mirror cover body W/LED 2pcs Edge cover of mirror 2pcs Extra wire set 2pcs Fuse set 2pcs Wire stripping quick splice connecter 4pcs Screw 16pcs Plug pin 4pcs |
| --- | --- |

2. Remove the factory mirror from your G class car. See picture 1

Picture 1

3. Remove the mirror body from the mirror holder. See picture 2 & 3

Picture 2                    Picture 3

4. Thread one steel wire to go along with the original cable for pulling the wire of the mirror cover body W/LED. See picture 4.

Thread the wire of the mirror cover body W/LED from the hole on the bottom of the original mirror body. See picture 5

Tie the steel wire together with the mirror cover LED wire then pulling the steel wire to let LED wire go through the hole. SEE picture 6.

Picture 4                Picture 5                Picture 6

5. Cover the mirror cover body W/LED on the original mirror body. See picture 7.

Picture 7

6. Cover the edge cover of mirror and put the screws to screw on the mirror cover W/LED body. See picture 8 & 9

Picture 7                        Picture 8

7. Fit the mirror W/LED body on the mirror holder. And that’s it! The mirror cover   W/ LED is upgrade and completed. See picture 9, 10 & 11

Picture 9                 Picture 10              Picture 11

8. Connect the wire at side lamp then re-install the mirror W/LED on your G class car and the door mirror cover W/LED is completed on the car.